## Slide 1: Project Overview
80 kg Autonomous Precision Agricultural Spraying UAV
This project presents the conceptual design of a heavy-lift quadcopter developed for autonomous crop spraying over large agricultural fields. The aircraft combines high payload capacity with precise navigation, controlled spray delivery, and automated mission execution.
Main Goals
Improve spray consistency and field coverage
Reduce operator workload and chemical exposure
Support repeatable autonomous spraying missions
Integrate flight, navigation, power, and spraying into one system
Design Focus: Precision • Efficiency • Safety • Autonomy

## Slide 2: Mission & Design Objectives
Mission
The UAV is designed to carry a liquid spray payload while following a planned route across agricultural fields. During the mission, it must maintain stable flight, accurate positioning, and controlled spray output while the operator supervises the system.
Main Objectives
Precision — Follow planned paths and maintain consistent coverage
Efficiency — Reduce unnecessary overlap, time, and spray use
Stability — Maintain controlled flight under high payload conditions
Safety — Monitor aircraft status and respond to system faults
Mission Flow;
Plan Mission → Take Off → Navigate → Spray → Return → Land

## Slide 3: Design Requirements
Parameter | Design Value
Maximum Takeoff Mass | ~80 kg
Spray Payload | 55 L
Empty Aircraft Mass | ~12 kg
Battery System | Dual LiPo, ~8 kg
Operating Speed | 5–7 m/s
Spray Width | ~5.5–6 m
Navigation | RTK-GPS
Flight Mode | Autonomous waypoint
Key Design Parameters
The aircraft requirements were derived from the intended agricultural mission and used as the basis for the engineering design. These values drive the sizing of the airframe, propulsion, power, avionics, and spraying systems.
Design Chain
Mission → Mass → Propulsion → Power → Control → Spraying

## Slide 4: Overall UAV Concept
Quad-X Configuration
The selected X-frame layout places four propulsion units symmetrically around a central body. The payload, batteries, and major electronics are arranged around the center of gravity to support stable flight and balanced mass distribution.
Main Elements
Structural frame
Four propulsion units
Central spray tank
Battery and power system
Flight-control electronics
Navigation sensors
Spray boom and nozzles
System Concept
Navigation → Flight Controller → Propulsion
Tank → Pump → Boom → Nozzles

## Slide 5: Propulsion System
Heavy-Lift Propulsion
At an MTOW of approximately 80 kg, the propulsion system must generate sufficient total thrust while retaining a practical thrust margin. The propulsion sizing was therefore based on rotor thrust, propeller operating conditions, motor power, and hover requirements.
Design Specifications
Configuration: 4 rotors
Operating condition: Hover + forward flight
Design point: Full aircraft mass
Sizing basis: Required thrust + safety margin
Propeller selection: Based on the calculated operating point
Motor selection: Matched to required thrust and power
Sizing Process
80 kg Aircraft → Required Thrust → Rotor Sizing → Motor → Propeller

## Slide 6: Power & Energy System
Balancing Power and Mass
The propulsion system creates the largest electrical demand, while avionics, sensors, and spraying equipment add additional loads. The selected dual-LiPo battery system of approximately 8 kg was incorporated into the aircraft mass and power budget.
Power Architecture
Dual LiPo → Power Distribution → ESCs → Motors
Battery → Regulators → Avionics + Sensors + Spray System
Design Considerations
Propulsion power demand
Battery capacity
Battery mass
Peak current demand
Avionics power
Mission energy requirement
The battery selection therefore represents a compromise between energy availability, endurance, and aircraft mass.

## Slide 7: Flight Performance
Designed for Agricultural Flight
The UAV is optimized for controlled, low-speed agricultural operation rather than maximum speed. Maintaining stable altitude, attitude, and forward motion is important because aircraft movement directly affects spray coverage.
Performance Specifications
Operating Speed: 5–7 m/s
Spray Width: ~5.5–6 m
Maximum Takeoff Mass: ~80 kg
Payload: 20 L
Typical Mission
Takeoff → Transit → Spray Pass → Turn → Spray Pass → Return → Landing
The performance target prioritizes stable coverage and controlled operation over high-speed flight.

## Slide 8: Avionics System
The UAV's Control Center
The avionics system connects the aircraft's sensors, navigation equipment, flight controller, propulsion system, and ground station. It processes information from the aircraft and turns mission commands into control actions.
Main Functions
Flight stabilization
Sensor processing
Navigation
Motor control
Autonomous mission execution
Telemetry
Failsafe management
Control Flow
Sensors → Flight Controller → ESCs → Motors
Flight Controller → Telemetry → Ground Station

## Slide 9: Navigation & Autonomous Flight
RTK-GPS Based Navigation
The UAV uses RTK-GPS to improve positioning accuracy during autonomous waypoint missions. Navigation data is combined with onboard motion sensing so the flight controller can track the planned route and maintain stable aircraft motion.
Navigation Specifications
Navigation: RTK-GPS
Flight Mode: Autonomous waypoint navigation
Mission Planning: Predefined field routes
Control: Closed-loop position feedback
Autonomous Mission
Mission Planning → Waypoints → Position Estimation → Flight Control → Feedback
The operator supervises the mission while the aircraft handles continuous stabilization and waypoint tracking.

## Slide 10: Sensors & State Estimation
Understanding the Aircraft's State
Autonomous flight requires continuous information about position, orientation, altitude, and motion. Since no single sensor provides all of this information, the flight controller combines several measurements to estimate the aircraft's current state.
Sensor Roles
RTK-GPS → Position
IMU → Motion + Attitude
Barometer → Altitude
Compass → Heading
Telemetry → System Status
This information forms the basis for stable flight and autonomous decision-making.

## Slide 11: Agricultural Spraying System
20 L Liquid Delivery System
The spraying subsystem stores and delivers the agricultural liquid through a controlled pump, flow system, and nozzle arrangement. The tank is integrated near the aircraft's central region to limit changes in balance as the liquid is consumed.
Specifications
Tank Capacity: 20 L
Spray Width: ~5.5–6 m
System: Tank + Pump + Filter + Boom + Nozzles
Control: Regulated liquid delivery
Spray Flow
20 L Tank → Filter → Pump → Flow Control → Boom → Nozzles → Crop
The spraying system is integrated with the UAV's flight mission rather than operating independently.

## Slide 12: Precision Spraying
Connecting Flight With Spray Quality
Spray consistency depends on the relationship between aircraft motion and liquid delivery. Speed, altitude, flow rate, nozzle arrangement, and spray width must therefore be considered together.
Control Relationship
Flight Speed + Altitude + Flow Rate → Spray Coverage
The design targets a spray width of approximately 5.5–6 m, while stable flight helps maintain consistent distance between the nozzles and crop.
Goal
Uniform Coverage • Controlled Application • Minimum Unnecessary Overlap

## Slide 13: Safety and reliability
Safety by Design
An approximately 80 kg autonomous aircraft carrying a 20 L liquid payload requires multiple layers of monitoring and failsafe protection. Abnormal conditions should trigger an appropriate response instead of allowing the aircraft to continue an unsafe mission.
Safety Functions
Battery monitoring
GPS/navigation monitoring
Communication monitoring
Return-to-home
Low-battery failsafe
Mission termination
Operator override
Pre-flight checks
Safety Logic
Fault Detected → Failsafe → Safe Flight Mode → Return / Land

## Slide 14: System Architecture
How the Subsystems Connect
The UAV is designed as an integrated system rather than a collection of independent components. The flight controller acts as the main connection between sensing, navigation, propulsion, autonomous control, and mission execution.
System-Level Flow
Dual LiPo → Power Distribution → Propulsion
RTK-GPS + Sensors → Flight Controller → Motor Control
Mission Planner → Ground Station → UAV
20 L Tank → Pump → Spray Boom
Core Architecture
Power → Compute → Control → Motion
Navigation → Decision → Flight
Payload → Delivery → Crop

## Slide 15: Data & Control Flow
A Closed-Loop Autonomous System
The aircraft continuously measures its actual condition and compares it with the desired mission state. The flight controller then adjusts the control commands to reduce errors and maintain the planned flight path.
Control Loop
Sensors → State Estimate → Flight Controller → Motor Commands → Aircraft Motion → Sensors
Mission Loop
Mission Plan → Waypoint Tracking → Position Feedback → Correction
This feedback structure allows the UAV to respond to disturbances instead of relying only on pre-programmed motor commands.

## Slide 16: Integrated 3D Design
Final Aircraft Concept
The final 3D model brings the structural frame, propulsion, payload, avionics, and spraying equipment together into one aircraft. This provides a practical visual check of how the different engineering decisions fit into the same physical platform.
Design Checks
Component interference
Propeller clearance
Tank placement
Spray-boom position
Ground clearance
Maintenance access
Overall proportions
NEBIYU SHOW OFF PLACE

## Slide 17: 3D Design & Airframe Layout
Turning the Concept Into a Physical Design
The 3D model translates the engineering concept into a physical aircraft arrangement. It allows component placement, balance, clearance, structural support, and access to be considered before physical construction.
Layout Priorities
Balanced mass distribution
Propeller clearance
Central payload placement
Battery accessibility
Protected electronics
Ground clearance
Clear spray path
Layout Principle
Payload + Battery + Electronics →
Central Region
Propulsion Units → Symmetric Around Center

## Slide 19: Simulation & Validation
Testing the Concept Before Flight
Simulation allows important aspects of the design to be studied before physical testing. It can help evaluate predicted behavior, identify possible weaknesses, and provide evidence for refining the aircraft.
Validation Process
Design → Simulation → Results → Comparison → Refinement
Analysis Areas
Propulsion performance
Flight behavior
Structural response
Power demand
Mission performance

## Slide 20: Results
What Does the Design Achieve?
The completed design brings the major engineering decisions together around the original agricultural mission. The preliminary analysis supports the feasibility of the proposed configuration while also showing where further physical validation is required.
Key Outcomes
~80 kg heavy-lift configuration established
20 L spray payload integrated
5–7 m/s operating range defined
~5.5–6 m spray width targeted
Dual-LiPo (~8 kg) power system incorporated
RTK-GPS autonomous navigation integrated
Propulsion sized around the full aircraft mass
Safety and monitoring functions included
Current Limitation
The design remains conceptual and requires detailed CAD, advanced simulation, prototype construction, and flight testing before real agricultural deployment.

## Slide 21: Conclusion
An Integrated Autonomous Spraying Platform
This project developed a conceptual ~80 kg autonomous agricultural spraying UAV by integrating the airframe, propulsion, power, avionics, navigation, spraying, and safety systems.
The key achievement is not simply the individual components, but their integration into one system designed around a real agricultural mission.
Final Mission
Carry Payload → Navigate Precisely → Spray Consistently → Monitor → Return Safely
Next Development
Detailed CAD → Simulation → Prototype → Ground Testing → Flight Testing
A complete UAV concept designed around precision, efficiency, and safe autonomous operation.

## Slide 22
Thank You!

## Slide 23
Group Members
Subgroup 5
Nebiyu Solomon Abebaw
CTC-1581-26
LEADER
Lijfikru Belete Wagaye
CTC-3088-26
Surafel bzuneh Tolcha
CTC-503-26
Ananya Melkamu Tessema
CTC-2847-26
Salahadin Hassen Haji
CTC-4441-26
Yodahe Leykun Assefa
CTC-119-26
Elbetel Taye Ladankilet
CTC-1610-26
Mekfira Abdulkadir Sherif
CTC-1837-26
Adonay Tetemke Fiseha
CTC-7358-26
Sifen Teshale
CTC-10111-26